## Slide 1
FPGA PROJECT
Pipelined Posit Multiplier implementation and comparison with IEE 754 floating point . (Group 23)
Github link : https://github.com/smartplay28/posit_multiplier
Team Members:
Akshat Mittal (IMT2023606)
Nachiappan (IMT2023605)

## Slide 2
Introduction
Posit number system is an emerging number system which aims to be a competitor to the existing IEEE floating-point number system.
It was introduced to provide higher accuracy and larger dynamic range for the same number of bits

## Slide 3
Posit multiplier Unlike IEEE 754, which has fixed-width fields for exponent and mantissa, Posit uses a dynamic bit allocation strategy.
This allows "Posits" to allocate more bits to the fraction (precision) when numbers are close to 1, and more bits to the exponent (range) when numbers are extremely large or small.
Methodology
Stage 1: Decode (Extraction)
Extract regime bits using Leading Zero/One Detector (LZOD) to determine run-length k
Separate sign bit, exponent e, and fraction f from the 32-bit Posit format
Stage 2: Execution (Core Computation)
Calculate output sign using XOR and compute total scale factor using adder logic
Perform mantissa multiplication (1.f_A) × (1.f_B) using FPGA DSP48 slices with pipelining
Stage 3: Encode (Packing)
Normalize the product by shifting fraction if result ≥ 2.0 and apply rounding
Re-pack the sign, regime, exponent, and fraction into final 32-bit Posit output

## Slide 4
Architecture of Posit Multiplier

## Slide 5
Results: Timing Summary

## Slide 6
Max Frequency

## Slide 7
Power Summary

## Slide 8
Resource Utilisation Summary

## Slide 10
Schematic

## Slide 11
Critical path
This is without clock divider
This is with clock divider
I implemented bitstream ila too issue related to that

## Slide 12
Comparison with IEE754 and posit multiplier
Basic info
Timing sumary

## Slide 13
Critical path
Power

## Slide 14
Resource utilization
Posit better for accuracy , dynamic range per bit and reduced errors for rest of all stuff as we can see critical path of posit is larger , power consumption is more , time taken is more , resources being used for posit is larger etc.